## Slide 1: Speech Signal Analysis
Ying shen
School of software engineering
Tongji university
Most slides come from http://www.inf.ed.ac.uk/teaching/courses/asr/2019-20/asr04-signal.pdf

## Slide 2: Content
Features for ASR
Spectral analysis
Cepstral analysis
Standard features for ASR: FBANK, MFCCs and PLP analysis
Dynamic features

## Slide 3: Speech signal analysis for ASR
Signal Analysis
Training Data
Acoustic Model
Language Model
Recorded Speech
Search Space
Decoded Text
(Transcription)

## Slide 4: A/D conversion
Convert analogue signals in digital form
Sound pressure wave
“你好”

## Slide 5: A/D conversion
Convert analogue signals in digital form
Microphone
Sound pressure wave
Conversion from impulse train to discrete−time sequence

## Slide 6: A/D conversion
Convert analogue signals in digital form
Microphone
Sound pressure wave
Conversion from impulse train to discrete−time sequence

## Slide 7: A/D conversion – Sampling
Things to know:
Sampling Frequency ()
Analogue low-pass filtering to avoid ‘aliasing’
NB: the cut-o frequency should be less than the Nyquist frequency (=)
Speech | Sufficient
Microphone voice (< 10kHz) | 20 kHz
Telephone voice (< 4kHz) | 8 kHz
Speech | 
Microphone voice (< 10kHz) | 20 kHz
Telephone voice (< 4kHz) | 8 kHz

## Slide 8: Nyquist-Shannon sampling theorem
The minimum sampling frequency of a signal that it will not distort its underlying information, should be double the frequency of its highest frequency component.
If is the sampling frequency, then the critical frequency (or Nyquist limit) is defined as equal to .
Notes: http://195.134.76.37/applets/AppletNyquist/Appl_Nyquist2.html

## Slide 9: Nyquist-Shannon sampling theorem
The minimum sampling frequency of a signal that it will not distort its underlying information, should be double the frequency of its highest frequency component.
If is the sampling frequency, then the critical frequency (or Nyquist limit) is defined as equal to .
Notes: http://195.134.76.37/applets/AppletNyquist/Appl_Nyquist2.html

## Slide 10: Nyquist-Shannon sampling theorem
Notes:
(1) In practice, the sampling rate is commonly selected in the range 2.5 ~4. For digital recording of music in CD a sampling rate of 44.1 kHz is commonly used.
(2) Prior to sampling, the signal must pass through a low-pass filter which will remove all unnecessary components (e.g. noise) higher than , preventing thus the “contamination” of the stored signal by their aliased frequencies.
Notes: http://195.134.76.37/applets/AppletNyquist/Appl_Nyquist2.html

## Slide 11: Acoustic Features for ASR
Speech signal analysis to produce a sequence of acoustic feature vectors
ASR
Front End
Acoustic Feature Vectors
Acoustic Model
Sampled signal

## Slide 12: Acoustic Features for ASR
Features should contain sufficient information to distinguish between phones
  Good time resolution (10ms)
  Good frequency resolution (20 ∼ 40 channels)
Be separated from and its harmonics
Be robust against speaker variation
Be robust against noise or channel distortions
Have good “pattern recognition characteristics”
  Low feature dimension
  Features are independent of each other (NB: this applies to GMMs, but not required for NN-based systems)
Notes: f0 – Also known as the fundamental frequency, f0 is a property of the source and is perceived by the ear as pitch. The f0 of the adult human voice ranges from 100-300 Hz.
The fundamental frequency or F0 is the frequency at which vocal chords vibrate in voiced sounds. This frequency can be identified in the sound produced, which presents quasi-periodicity, the pitch period being the fundamental period of the signal (the inverse of the fundamental frequency). Pitch is more often used to refer to how the fundamental frequency is perceived.

## Slide 13: MFCC-based front end for ASR
A/D Conversion
Preempahsis
Windowing
DFT
Mel filterbank
log()
DCT
Dynamic
features
Feature Transform
Acoustic Model
Energy
Notes: https://haythamfayek.com/2016/04/21/speech-processing-for-machine-learning.html
https://wiki.aalto.fi/display/ITSP/Cepstrum+and+MFCC

## Slide 14: Pre-emphasis and spectral tilt
Pre-emphasis increases the magnitude of higher frequencies in the speech signal compared with lower frequencies
Spectral Tilt
  The speech signal has more energy at low frequencies (for voiced speech)
  This is due to the glottal source (see the figure)
Pre-emphasis (first-order) filter boosts higher frequencies:
Notes: 语音信号的预加重，目的是为了对语音的高频部分进行加重，去除口唇辐射的影响，增加语音的高频分辨率。对于语音信号，我们需要进行这步是因为高频信号的信息量更大。一般来说元音的频率更低，辅音的频率更高。假如给你一个单词 Microsoft，如果只保留辅音部分 Mcsft，还是可以明白它表达了什么，这就是为什么说辅音的信息量更大。

## Slide 15: Speech production model
Notes: 语言发音模型的理论基础是言语产生的声学理论。根据 Stevens 的观点，声门把气流通道分成了上下两部分，对于大多数语音的产生过程而言，声门以下的系统提供了气流能量，喉部和声门以上的结构对气流进行调制，产生可以听到的声音。经过对语音进行深入研究，学者们普遍认为：（1）由声带震动产生周期信号，通过声道共鸣，形成浊音；（2）由气流爆破或者摩擦产生非周期噪声，形成清音；（3）清音和浊音经过唇、鼻辐射，在空间进行传播，形成语音。根据这种理论，只要掌握了声源、共鸣、辐射的声学规律，就可以模拟语音的产生过程。

## Slide 16: Pre-emphasis and spectral tilt
Notes: 你好.wav

## Slide 17: Windowing
The speech signal is constantly changing (non-stationary)
Signal processing algorithms usually assume that the signal is stationary
Piecewise stationarity: model speech signal as a sequence of frames (each assumed to be stationary)

## Slide 18: Windowing
Windowing: multiply the full waveform by a window (in time domain):
Simply cutting out a short segment (frame) from is a rectangular window – causes discontinuities at the edges of the segment

## Slide 19: Windowing
Instead, a tapered window is usually used e.g. Hamming () or Hanning () window

## Slide 20: Windowing

## Slide 21: Windowing
Window the signal into frames and apply Fourier Transform to each segment.
  Short frame width: wide-band, high time resolution, low frequency resolution
  Long frame width: narrow-band, low time resolution, high frequency resolution
For ASR:
  frame width ∼ 25ms
  frame shift ∼ 10ms
windowing
t-th frame
0
L-1
Windowed signal
Notes: 宽带spectrogram: 以3ms(或300Hz左右的带宽)左右进行分帧之后制成的spectrogram
窄带spectrogram: 以20ms(或45Hz左右的带宽)左右进行分帧之后制成的spectrogram
对于τ=3 ms , 对应带宽为293Hz,
对于τ=20 ms ，对应带宽为44Hz.

## Slide 22: Windowing
Window the signal into frames and apply Fourier Transform to each segment.
  Short frame width: wide-band, high time resolution, low frequency resolution
  Long frame width: narrow-band, low time resolution, high frequency resolution
For ASR:
  frame width ∼ 25ms
  frame shift ∼ 10ms
windowing
t+1-th frame
0
L-1
shift
Windowed signal

## Slide 23: Discrete Fourier Transform (DFT)
Purpose: extracts spectral information from a windowed signal (i.e. how much energy at each frequency band)
Input: windowed signal (time domain)
Output: a complex number for each of frequency bands representing magnitude and phase for the k-th frequency component (frequency domain)
Discrete Fourier Transform (DFT):
Fast Fourier Transform (FFT) — efficient algorithm for computing DFT when is a power of 2, and .

## Slide 24: DFT Spectrum
25ms Hamming window of “你好” speech (sample rate = 44100HZ) and its spectrum computed by DFT
Notes: Window size = 1102 fft length=16384
“你好”5000-6102采样点

## Slide 25: Windowing and spectral analysis
windowing
t-th frame
0
L-1
FFT
Window the signal into frames and apply Fourier Transform to each segment.
  Short frame width: wide-band, high time resolution, low frequency resolution
  Long frame width: narrow-band, low time resolution, high frequency resolution
For ASR:
  frame width ∼ 25ms
  frame shift ∼ 10ms
Frequency
Magnitude
Short−time power spectrum

## Slide 26: Windowing and spectral analysis
FFT
windowing
t+1-th frame
0
L-1
shift
Window the signal into frames and apply Fourier Transform to each segment.
  Short frame width: wide-band, high time resolution, low frequency resolution
  Long frame width: narrow-band, low time resolution, high frequency resolution
For ASR:
  frame width ∼ 25ms
  frame shift ∼ 10ms
Frequency
Magnitude
Short−time power spectrum

## Slide 27: Wide-band and narrow-band spectrograms
Narrow band spectrogram
Window width = 20ms
Wide band spectrogram
Window width = 2ms
Notes: 1. Sample points=132; noverlap=66,nfft=256
2. Sample points=882; noverlap=441,nfft=1024

## Slide 28: MFCC-based front end for ASR
A/D Conversion
Preempahsis
Windowing
DFT
Mel filterbank
log()
DCT
Dynamic
features
Feature Transform
Acoustic Model
Energy

## Slide 29: Human hearing
Technical terms
  equal-loudness contours
  Masking
  auditory filters (critical-band filters)
  critical bandwidth
Physical quality | Perceptual quality
Intensity | Loudness
Fundamental frequency | Pitch
Spectral shape | Timbre
Onset/offset time | Timing
Phase difference in binaural hearing | Location

## Slide 30: Equal loudness contour

## Slide 31: Nonlinear frequency scaling
Human hearing is less sensitive to higher frequencies -- thus human perception of frequency is nonlinear
Bark scale
Mel scale
Notes: The mel scale, named by Stevens, Volkmann, and Newman in 1937,[1] is a perceptual scale of pitches judged by listeners to be equal in distance from one another. The reference point between this scale and normal frequency measurement is defined by assigning a perceptual pitch of 1000 mels to a 1000 Hz tone, 40 dB above the listener's threshold. Above about 500 Hz, increasingly large intervals are judged by listeners to produce equal pitch increments. As a result, four octaves on the hertz scale above 500 Hz are judged to comprise about two octaves on the mel scale. The name mel comes from the word melody to indicate that the scale is based on pitch comparisons.

## Slide 32: Mel-Filter Bank
Each filter in the filter bank is triangular having a response of 1 at the center frequency and decrease linearly towards 0 till it reaches the center frequencies of the two adjacent filters where the response is 0
Notes: This is a set of 20-40 (26 is standard) triangular filters that we apply to the periodogram power spectral estimate from step 2
M是滤波器个数；K_bm是滤波器的临界频率；K是DFT变换的点数
http://practicalcryptography.com/miscellaneous/machine-learning/guide-mel-frequency-cepstral-coefficients-mfccs/

## Slide 33: Mel-Filter Bank
Apply a mel-scale filter bank to DFT power spectrum to obtain mel-scale power spectrum
Each filter collects energy from a number of frequency bands in the DFT
Linearly spaced < 1000 Hz, logarithmically spaced > 1000 Hz
DFT(STFT) power spectrum
1
2
N
Frequency bins
Triangular band−pass filters
 |  | … |  | … | 
1
2
M
Mel-scale power spectrum

## Slide 34: Mel-Filter Bank
Apply a mel-scale filter bank to DFT power spectrum to obtain mel-scale power spectrum
Each filter collects energy from a number of frequency bands in the DFT
Linearly spaced < 1000 Hz, logarithmically spaced > 1000 Hz
DFT(STFT) power spectrum
1
2
N
Frequency bins
Triangular band−pass filters
 |  | … |  | … | 
1
2
M
Mel-scale power spectrum

## Slide 35: Mel-Filter Bank
Apply a mel-scale filter bank to DFT power spectrum to obtain mel-scale power spectrum
Each filter collects energy from a number of frequency bands in the DFT
Linearly spaced < 1000 Hz, logarithmically spaced > 1000 Hz
DFT(STFT) power spectrum
1
2
N
Frequency bins
Triangular band−pass filters
 |  | … |  | … | 
1
2
M
Mel-scale power spectrum

## Slide 36: Mel-Filter Bank
Apply a mel-scale filter bank to DFT power spectrum to obtain mel-scale power spectrum
Each filter collects energy from a number of frequency bands in the DFT
Linearly spaced < 1000 Hz, logarithmically spaced > 1000 Hz
DFT(STFT) power spectrum
1
2
N
Frequency bins
Triangular band−pass filters
 |  | … |  | … | 
1
2
M
Mel-scale power spectrum

## Slide 37: Mel-Filter Bank
Apply a mel-scale filter bank to DFT power spectrum to obtain mel-scale power spectrum
Each filter collects energy from a number of frequency bands in the DFT
Linearly spaced < 1000 Hz, logarithmically spaced > 1000 Hz
DFT(STFT) power spectrum
1
2
N
Frequency bins
Triangular band−pass filters
 |  | … |  | … | 
1
2
M
Mel-scale power spectrum

## Slide 38: An example of Mel-Filter Bank computation
The example will use 10 filterbanks because it is easier to display, in reality you would use 26-40 filterbanks.
  Choose a lower and upper frequency: 300Hz~8000Hz (Suppose sample rate is 16KHz)
  Using Eq. 1, convert the upper and lower frequencies to Mels. In our case 300Hz is 401.25 Mels and 8000Hz is 2834.99 Mels.
  Because we will do 10 filterbanks, for which we need 12 points. This means we need 10 additional points spaced linearly between 401.25 and 2834.99. This comes out to:
  Now use Eq. 2 to convert these back to Hertz:
= 401.25, 622.50, 843.75, 1065.00, 1286.25, 1507.50, 1728.74, 1949.99, 2171.24, 2392.49, 2613.74, 2834.99
(1)
(2)
= 300, 517.33, 781.90, 1103.97, 1496.04, 1973.32, 2554.33,3261.62, 4122.63, 5170.76, 6446.70, 8000

## Slide 39: An example of Mel-Filter Bank computation
The example will use 10 filterbanks because it is easier to display, in reality you would use 26-40 filterbanks.
  Suppose DFT has 512 bins. Round those frequencies to the nearest FFT bin.
  Now we create our filterbanks.
(3)
= 9, 16, 25, 35, 47, 63, 81, 104, 132, 165, 206, 256

## Slide 40: An example of Mel-Filter Bank computation
A Mel-filterbank containing 10 filters. This filterbank starts at 0Hz and ends at 8000Hz. This is a guide only, the worked example above starts at 300Hz.

## Slide 41: Mel-Filter Bank (Cont.)
How many number of mel-filter channels?
for GMM-HMM based ASR
for DNN-HMM based ASR
where k: DFT bin number (1,…,N)
m: mel-filter bank number (1,…,M)

## Slide 42: MFCC-based front end for ASR
A/D Conversion
Preempahsis
Windowing
DFT
Mel filterbank
log()
DCT
Dynamic
features
Feature Transform
Acoustic Model
Energy

## Slide 43: Log Mel Power Spectrum
Compute the log magnitude squared of each mel-filter bank output:
  Taking the log compresses the dynamic range
  Human sensitivity to signal energy is logarithmic -- i.e. humans are less sensitive to small changes in energy at high energy than small changes at low energy
  Log makes features less variable to acoustic coupling variations
  Removes phase information -- not important for speech recognition (not everyone agrees with this)
Aka “log mel-filter bank outputs” or “FBANK features”, which are widely used in recent DNN-HMM based ASR systems

## Slide 44: MFCC-based front end for ASR
A/D Conversion
Preempahsis
Windowing
DFT
Mel filterbank
log()
DCT
Dynamic
features
Feature Transform
Acoustic Model
Energy
Notes: http://www.speech.cs.cmu.edu/15-492/slides/03_mfcc.pdf

## Slide 45: DFT Spectrum Features for ASR
Equally-spaced frequency bands -- but human hearing less sensitive at higher frequencies (above ~ 1000Hz)
The estimated power spectrum contains harmonics of F0, which makes it difficult to estimate the envelope of the spectrum
Frequency bins of STFT are highly correlated each other, i.e. power spectrum representation is highly redundant
Notes: ①“基频：指一个复杂声波中最低的一个频率（其他频率叫谐波）。‘基频’即F0，对语调的研究特别重要，语调中的基频与涉及的音高变化之间有相当紧密的对应关系。”（《现代语言学词典》） ②“基音的振动频率叫基频，它决定语音音调的高低；陪音的频率叫谐波频率，它们决定语音的音色区别。因此，两个具有相同的基频的语音可以因为谐波频率不同而具有不同的音色；相反，两个相同音色的语音可以因为基频的不同而具有不同的音高。”《语言文字学常用辞典》）

## Slide 46: Cepstral Analysis
Source-Filter model of speech production
  Source: Vocal cord vibrations create a glottal source waveform
  Filter: Source waveform is passed through the vocal tract: position of tongue, jaw, etc. give it a particular shape and hence a particular filtering characteristic
Source characteristics (F0, dynamics of glottal pulse) do not help to discriminate between phones
The filter specifies the position of the articulators
... and hence is directly related to phone discrimination
Cepstral analysis enables us to separate source and filter

## Slide 47: Speech production model

## Slide 48: Cepstral Analysis
Split power spectrum into spectral envelope and F0 harmonics.
Log spectrum (freq domain)
Inverse Fourier Transform
Cepstrum (time domain) (quefrency)
Liftering to get low/high part
(lifter: filter used in cepstral domain)
Fourier Transform
Smoothed log spectrum (freq domain)
[low-part of cepstrum]
+
Fine structure
[high-part of cepstrum]
Notes: Cepstrum serves as a tool to investigate periodic structures in frequency spectra
The term cepstrum was derived by reversing the first four letters of spectrum. Operations on cepstra are labelled quefrency analysis (or quefrency alanysis), liftering, or cepstral analysis.

## Slide 49: The Cepstrum
Cepstrum obtained by applying inverse DFT to log magnitude spectrum (may be mel-scaled)
Cepstrum is time-domain (we talk about quefrency)
Inverse DFT:
Since log power spectrum is real and symmetric the inverse DFT is equivalent to a discrete cosine transform (DCT)
is the number of MFCCs

## Slide 50: MFCCs
Smoothed spectrum: transform to cepstral domain, truncate, transform back to spectral domain
Mel-frequency cepstral coecients (MFCCs): use the cepstral coecients directly
  Widely used as acoustic features in HMM-based ASR
  First 12 MFCCs are often used as the feature vector (removes F0 information)
  Less correlated than spectral features – easier to model than spectral features
  Very compact representation – 12 features describe a 20ms frame of data
  For standard HMM-based systems, MFCCs result in better ASR performance than filter bank or spectrogram features
  MFCCs are not robust against noise

## Slide 51: MFCC-based front end for ASR
A/D Conversion
Preempahsis
Windowing
DFT
Mel filterbank
log()
DCT
Dynamic
features
Feature Transform
Acoustic Model
Energy

## Slide 52: Dynamic features
Speech is not constant frame-to-frame, so we can add features to do with how the cepstral coefficients change over time
, are delta features (dynamic features / time derivatives)
Simple calculation of delta features at time for cepstral feature :
More sophisticated approach estimates the temporal derivative by using regression to estimate the slope (typically using 4 frames each side)
“Standard” ASR features (for GMM-based systems) are 39 dimensions:
  12 MFCCs, and energy
  12 ΔMFCCs, Δenergy
  12 Δ2MFCCs, Δ2energy

## Slide 53: MFCC-based front end for ASR
A/D Conversion
Preempahsis
Windowing
DFT
Mel filterbank
log()
DCT
Dynamic
features
Feature Transform
Acoustic Model
Energy

## Slide 54: Feature normalization
Basic Idea: Transform the features to reduce mismatch between training and test
Cepstral Mean Normalization (CMN): subtract the average feature value from each feature, so each feature has a mean value of 0. makes features robust to some linear filtering of the signal (channel variation)
Cepstral Variance Normalisation (CVN): Divide feature vector by standard deviation of feature vectors, so each feature vector element has a variance of 1
Cepstral mean and variance normalization, CMN/CVN:
Compute mean and variance statistics over longest available segments with the same speaker/channel
Real time normalization: compute a moving average

## Slide 55: An example of MFCC computation
We start with a speech signal , we'll assume sampled at 16kHz.
1. Frame the signal into 20-40 ms frames. 25ms is standard. Frame step is usually 10ms.
  0.025*16000 = 400 samples
  Denote the -th frame , where ranges over 1-400
2. Take the Discrete Fourier Transform of the frame
  , is a hamming window with 400 length, is the length of DFT (e.g. 512)
  The power spectrum
  We would generally perform a 512 point FFT and keep only the first 257 coefficents
Notes: http://practicalcryptography.com/miscellaneous/machine-learning/guide-mel-frequency-cepstral-coefficients-mfccs/
1. The first 400 sample frame starts at sample 0, the next 400 sample frame starts at sample 160 etc.

## Slide 56: An example of MFCC computation
3. Compute the Mel-Filter Bank
  This is a set of 20-40 (26 is standard) triangular filters that are applied to
  Multiply each filterbank with , then add up the coefficents
  26 numbers are left indicating of how much energy was in each filterbank.
4. Take the log of each of the 26 energies
5. Take the Discrete Cosine Transform (DCT) of the 26 log filterbank energies to give 26 cepstral coefficents . For ASR, only the lower 12 of the 26 coefficients are kept.
6. Compute energy for
7. Compute and for and energies ,
Notes: 3. Our filterbank comes in the form of 26 vectors of length 257 (assuming the FFT settings from step 2). Each vector is mostly zeros, but is non-zero for a certain section of the spectrum.

## Slide 57: Acoustic features in state-of-the-art ASR systems
See Tables 1, 2, and 3 in
Jinyu Li, Dong Yu, Jui-Ting Huang, and Yifan Gong, “Improving Wideband Speech Recognition Using Mixed-Bandwidth Training Data In CD-DNN-HMM”,
2012 IEEE Workshop in Spoken Language Technology (SLT2012).
https://doi.org/10.1109/SLT.2012.6424210

## Slide 61: Summary: Speech Signal Analysis for ASR
Good characteristics of ASR features
FBANK features
  Short-time DFT analysis
  Mel-filter bank
  Log magnitude squared
  Widely used for DNN ASR ()
MFCCs-mel frequency cepstral coefficients
  FBANK features
  Inverse DFT (DCT)
  Use first few (12) coecients
  Widely used for GMM-HMM ASR
Delta features (dynamic features)
39-dimension feature vector (for GMM-HMM ASR): MFCC-12 + energy; + Deltas; + Delta-Deltas

## Slide 62: References
J&M: Daniel Jurafsky and James H. Martin (2008). Speech and Language Processing, Pearson Education (2nd edition).
Taylor: Paul Taylor (2009). Text-to-Speech Synthesis, Cambridge University Press.
Hynek Hermansky, “Perceptual linear predictive (PLP) analysis of speech,” The Journal of the Acoustical Society of America, Vol.87, No.4, pp.1737-1752, 1980.

## Slide 63: Assignment 1
Extract acoustic features (MFCC) for a segment of speech. Comment your codes properly.
Processing steps include:
  Pre-emphasis
  Windowing
  STFT
  Mel-filter bank
  Log()
  DCT
  Dynamic feature extraction
  Feature transformation